## PUNJAB STATE POWER CORPORATION LIMITED

(Regd. Office : PSEB Head Office, The Mall, Patiala – 147001)

Corporate identity Number U40109PB2010SGC033813 Website: wwwpspcl.in

GURU GOBIND SINGH SUPER THERMAL PLANT ROOPNAGAR

Tender Notice.

| Office | Chief Engineer GGSSTP, Roopnagar. |
| --- | --- |
| Tender Specification No. | 6828 /P-3/EMP-10941 Dated: 01.09.15 |
| Issuing Authority | Chief Engineer /GGSSTP, Roopnagar. |
| Address: | Dy.CE/Monitoring, GGSSTP Roopnagar. |
| Place | Roopnagar. |
| Short Description | Procurement of electrolyte cell for hydrogen gas plant stage-I & III in GGSSTP Roopnagar. |
| Tender publication | ON ALL INDIA BASIS |
| Eligibility Criteria | As per terms and conditions |
| 1)Last Date for Sale of Documents | 05.10.2015 up to 11.00 A.M. |
| 2) Last Date of Bid Submission | 08.10.2015 up to 11.00 A.M. |
| 3) Bid Opening | 08.10.2015 at 11.30 A.M. |
| Document Cost | Rs. 500/- |
| Payment Mode | DD or Cash |
| Payment in favour of | Accounts Officer/O&M, GGSSTP, Roopnagar. (PUNJAB) |
| EMD | Demand Draft in favour of Accounts Officer/O&M, GGSSTP, Roopnagar (PUNJAB) |
| Contact No. | Phone No. 01881-275666 FAX No. 01881-274232 |

Tender Details:-

| Sr. No. | Description | Qty. (No’s) |
| --- | --- | --- |
|  | Water Electrolytic cell for generation of hydrogen gas having generating cell capacity 0.85 NM3 /Hr., 99.9% purity, 9 bells (5 cathodes + 4 anodes) with D.C. current 2000 amps. 2.5 volts per cell. Dimensions of cell-1245 mm x 508 mm x 762 mm made out of M.S sheet along with cooling coils with epoxy painted. | 4 |

TERMS AND CONDITIONS

- A set of tender documents containing detailed technical specifications, General instructions and terms & conditions can be obtained from Dy.CE/Monitoring, V&P.O. Ghanauli, GGSSTP, Roopnagar -140113 on payment of cost by cash or demand draft drawn in favour of Accounts officer/O&M, GGSSTP, Roopnagar payable at Roopnagar (PUNJAB)

- Tender of firms, which do not purchase the tender documents in advance, shall not be opened.

- All tenders must be accompanied by earnest money at the rates prescribed in the tender documents except in the case of those tenderers who are specifically exempted there under.

- Telegraphic / Fax quotations shall not be accepted.

- Negotiations shall not be held, except with the lowest tenderer.

SE/ Monitoring,

GGSSTP, Roopnagar.